## Slide 1: Preliminary Confidence Testing Results
June 27, 2014

## Slide 2: Topics
What river concentrations can we expect at low flow?
What do current confidence testing results tell us?

## Slide 3: What River Concentrations Can We Expect at Low Flow?
Many PCB sources to Spokane River are independent of flow
As river flows drop, these sources get diluted less
  River PCB concentrations will go up
We can use existing PCB measurements at higher flow to estimate concentrations at low flow

## Slide 4: Mathematical Basis
Concentration = Total PCB Load ÷ Total Flow
  Total PCB load comprised of
    Load from Lake Coeur d’Alene
    Relatively constant loads (e.g. WWTPs)
    Flow-dependent loads (e.g. stormwater)

## Slide 5: Mathematical Basis
Back-calculate constant loads from existing monitoring studies
  Constant loads = Total observed load – load from Lake Coeur d’Alene – stormwater loads
    Total observed load: Observed concentration x total flow
    Load from Lake Coeur d’Alene: Assumed (low) concentration x flow at Coeur d’Alene
    Stormwater loads: estimated from Ecology Source Assessment

## Slide 6: Mathematical Basis
Project future concentration at lower flow
  Concentration = Total PCB Load ÷ Total Flow
  Concentration = (Load from Lake Coeur d’Alene + Constant loads) ÷ Total Flow

## Slide 7: Data Sources
Ecology PCB Source Assessment (2013)
  SPMD data from 2003-2004
Era-Miller (2014)
  Grab and CLAM data from 10/2012, 5/2013

## Slide 8: Results
 | Dry Weather Load (mg/day) |  |  |  | Concentration at 1000 cfs (pg/l) |  |  | 
 | 03/4S | 10/12G | 10/12C | 5/13G | 03/4S | 10/12G | 10/12C | 5/13G
Stateline | 432 |  |  | 61 | 177 |  |  | 25
Upriver | 492 |  | 224 | 345 | 201 |  | 92 | 141
Ninemile | 1519 | 51 | 644 | 944 | 621 | 21 | 264 | 386
03/4S: 2003-2004 SPMD 10/12G: Oct. 2012 Grab 10/12C: Oct. 2012 Clam 5/13G: May 2013 Grab |  |  |  |  |  |  |  | 
Projected concentrations (pg/l) at 1000 cfs
  Stateline: 101
  Upriver: 145
  Ninemile: 323

## Slide 9: What Do Current Confidence Testing Results Tell Us?
Still waiting on final QA results from AXYS
Rough calculations indicate that data will not be sufficient to quantitatively define incremental loads (e.g. groundwater)
  ~30% change in concentrations between stations is required for us to detect it with confidence
  Data will be suitable for qualitative assessment (e.g. is groundwater significant?)