## Slide 1: Suitability of Spokane River data for fingerprinting
Lisa RODENBURG
Department of Environmental Sciences, Rutgers, the State University of New Jersey, 14 College Farm Road, New Brunswick, NJ 08901
* Presenting Author: Telephone: 848-932-5774 Fax: 732-932-8644, lisa.rodenburg@rutgers.edu

## Slide 2: Problem
Where are the PCBs in the Spokane River coming from?
Many ways to answer this:
  Sampling of suspected sources
  Mass balance
  Water quality modeling
  Fingerprinting

## Slide 3: Fingerprinting
Primary sources
  Fingerprints might resemble unweathered Aroclors
Secondary sources
  Fingerprints might resemble weathered Aroclors
  Fingerprints might include some non-Aroclor congeners
Weathering processes can include:
  Anaerobic dechlorination might implicate sewers/groundwater
  Cytochrome P450 metabolism is expected in organisms; might be able to correct for this to identify the parent Aroclors
  Loss of high or low MW congeners due to volatilization, sorption
  Other?????? Weathering is complex

## Slide 4: Ways to do fingerprinting
Positive Matrix Factorization
  Requires larger data set, ideally >50 samples
Multiple Linear Regression
Both approaches require high quality data:
  1668 preferably
  SPB-octyl column preferred
  We have Aroclors measured on SGE-HT8 as well
  Most congeners are detected
  Detection limits are known

## Slide 5: Available data sets

## Slide 6: Data sets
Plenty of data for PMF:
  Surface water
  Storm water
  Fish
  Kaiser outfall
  Kaiser groundwater
  SCRWRF influent
Small data sets suitable for MLR:
  Atmospheric deposition (probably lump with Green-Duwamish for PMF)
  Sediment
  Surface water CLAM
  Biofilm
  GE Groundwater
  Groundwater seeps

## Slide 7: Very preliminary findings
Fish are dominated by Aroclors 1254 and 1260
  These higher MW Aroclors bioaccumulate most effectively
Fish and invertebrates show evidence of cytochrome P450 metabolism
  But you can still recognize that 1254 and 1260 were the parent Aroclors
Dechlorination might occur in Kaiser groundwater
  might help us track this source;
  no dechlorination signal observed in the surface water)
Surface water Aroclors appear largely unweathered